## Slide 1
Erik Moll
Philips Research
September 2022
ACOM and GHS
A unified model for personal health device communication
Supported on Bluetooth LE

## Slide 2: The problem
Personal health devices are abundantly available in most markets and are quite often connected and come with an application running on a smart phone, a tablet or sometimes a PC.
In most cases Bluetooth (Low Energy) is used to connect these devices. Sometimes USB, Wi-Fi or cellular connectivity is supported.
For remote patient monitoring, personal health & fitness tracking and many other use cases it is desired to integrate data from such devices in one place, one service for the patient or user.
Today, September 2022, there is still no good, generic, interoperable standard solution for personal health device communication.
As a result, for each PHD dedicated software is needed in devices, apps, gateways, servers => costly!
Personal Health Devices
Proprietary apps and gateways
Proprietary protocols over Bluetooth ®
Cloud-based
proprietary services
Proprietary Direct-to-Cloud (D2C) protocols
Proprietary data upload and retrieval
Proprietary data upload and retrieval
Proprietary data upload and retrieval
Proprietary protocols over Bluetooth ®
Proprietary protocols over Bluetooth ®
Proprietary Direct-to-Cloud (D2C) protocols
Cloud-based
proprietary services

## Slide 3: The solution
HL7 FHIR:
  The healthcare IT world is moving towards HL7 FHIR as the application-level language to achieve interoperability of healthcare data in and around the hospital.
  Regulations in US and EU require healthcare IT systems to open up their data via a FHIR interface
  This helps a lot but does not yet solve the PHD communication diversity and that is where ACOM comes into play.
IEEE 11073-10206 ACOM:
  ACOM stands for “Abstract Content Model”
  ACOM defines a model based on the IEEE 11073 Domain Information Model (DIM) and nomenclature standard for medical device communication
  ACOM objects and attributes map 1-1 to HL7 FHIR resources using JSON or XML.
  ACOM is implemented in a binary protocol on Bluetooth LE – the Generic Health Sensor profile and service (GHS).
  ACOM can be used by cellular IoT health sensor devices using a binary or JSON format
Within various working groups of IEEE, IHE and the Bluetooth SIG we developed the ACOM specification and protocols using it.

## Slide 4: The solution: ACOM + FHIR
Build once
  ACOM + FHIR enable a generic solution to connect sensor devices to apps, gateways and to cloud services
Extendable / flexible solution
  Sensor types can be added without coding in apps / gateways / servers
  The set of supported Observations can be extended without coding
  Many device types / specializations are defined already in IEEE 11073 in an ACOM-compatible manner
Enables an end-to-end ecosystem
  Based on one conceptual model of health devices and generated observations using a recognized nomenclature system
  Suitable for [personal] health sensor devices at home, in the hospital and elsewhere (health & fitness, elderly care)
Personal Health Devices
Generic apps and gateways
ACOM / GHS @ Bluetooth (LE)
FHIR servers
Direct-to-Cloud (D2C) ACOM/FHIR upload
IHE FHIR Observation upload and retrieval

## Slide 5: IEEE 11073-10206 - ACOM basics
ACOM defines a simple information model for PHDs

## Slide 6: ACOM Observations
ACOM supports the common classes of observations from PHDs
ACOM is a toolbox to define observation profiles that your device type supports

## Slide 7: ACOM Observation mapped to FHIR Observation resource
Example ACOM & FHIR SpO2 Observation
Mapping is following the HL7 FHIR PHD Implementation Guide and the IHE PHD Observation Upload (POU) profile
ACOM Observation attribute | Value | FHIR Observation attribute & value
Object | Numeric Observation | { “resourceType”: “Observation”,
Type | MDC_PULS_OXIM_SAT_O2 (2::19384) | “code”: {“coding”: [{ “system”: “urn:iso:std:iso:11073:10101”, “code”: “150456” }]},
Unit Code | MDC_DIM_PERCENT (4::544) | “valueQuantity”:{ “system”: “urn:iso:std:iso:11073:10101”, “code”: “262688”, “value”: 89.0 },
Observed Value | 89.0 | 
Time stamp | 2017-09-04 16:30:00 +1:00 (1504542600) | “effectiveDateTime”: “2017-09-04T16:30:00+01:00” }

## Slide 8: Bluetooth GHS GATT profile and service specifications
Generic Health Sensor Client / Collector
Generic Health Sensor Server / Sensor
GATT
Generic Health Sensor Service
Elapsed Time Service
Observations
Device Information
Time
Power status
User Information
Simple to implement on constrained devices
Device Info Service 1.2
Battery Service 1.1
User Data Service 1.1
Reconnection config 1.0
Connection parameters

## Slide 9
Philips ACOM/GHS prototypes – used for interop testing
Health Observations
Device information
LE / GATT / GHS
Time and power information
Open-sourced
https://github.com/philips-labs/BLE-GHS-Server-Simulator
Post Observations

## Slide 10: Summary
We introduced the IEEE Abstract Content Model for Personal Health Devices – ACOM in the context of HL7 FHIR-based healthcare systems:
ACOM solves a big interoperability problem and enables an ecosystem of connected personal health devices, apps, services
The Bluetooth SIG Generic Health Sensor service and profile specification support ACOM on top of Bluetooth LE.
Some details:
  IEEE 11073-10206 - ACOM defines a generic model for personal health devices and the observations these devices can generate
  ACOM objects in this model can easily be mapped to FHIR resources
  The Bluetooth Generic Health Sensor service and profile are based on ACOM and are in interop testing phase in the SIG
  ACOM and GHS enable build-once gateways to get PHD Observations into FHIR servers
  GHS demonstrators and source code are available on Android